## Slide 1
The term, "chromatography" was coined by the Russian botanist, Tswett, who demonstrated that, when a plant extract was carried by petroleum ether through a column consisting of a glass tube packed with calcium carbonate powder, a number of dyes were separated, as shown in Figure below . He named this analysis method "Chromatographie" after "chroma" and "graphos", which are Greek words meaning "color" and "to draw," respectively
Principle of High performance liquid chromatography HPLC
Figure 1. Diagram showing Tswett's experiment

## Slide 2
High Performance Liquid Chromatography, (HPLC)
High performance liquid chromatography or commonly known as HPLC is A very sensitive and accurate analytical technique for analyzing mixtures and used to separate, identify or quantify each component in a mixture.
In the 1960s the column chromatography LC with its low-pressure suitable glass columns was further developed to the HPLC with its high-pressure adapted metal columns
The mixture is separated using the basic principle of column chromatography and then identified and quantified by spectroscopy.
HPLC is thus basically a highly improved form of column liquid chromatography. Instead of a solvent being allowed to drip through a column under gravity, it is forced through under high pressures of up to 400 atmospheres.

## Slide 3
HPLC usually preferred over other methods used in quantitative analysis, where we obtain accurate qualitative separation of the components of the mixture to be identified.
This technique is often used in biochemistry and analytical chemistry to separate, identify, and quantify compounds in one mixture.
The compounds are separated by injecting a sample mixture onto the column. The different component in the mixture passes through Column at differentiation due to differences in the behavior of components in the sample between the mobile phase and the stationary phase.
The mobile phase should be discarded to eliminate the formation of air bubbles

## Slide 4
The main components of the HPLC device:
High pressure pump
Injector
Chromatographic column
Detector
Personal computer to read data of component

## Slide 5
Pump:
The role of the pump is to force a liquid (called the mobile phase) through the liquid chromatograph at a specific flow rate, expressed in milliliters per min (mL/min).
Normal flow rates in HPLC are in the 1- to 2-mL/min range.
Typical pumps can reach pressures in the range of 6000-9000 psi (400- to 600-bar).
During the chromatographic experiment, a pump can deliver a constant mobile phase composition (isocratic) or an increasing mobile phase composition (gradient)

## Slide 6
Injector:
The injector serves to introduce the liquid sample into the flow stream of the mobile phase.
Typical sample volumes are 5- to 20-microliters (µL).
The injector must also be able to withstand the high pressures of the liquid system.
An autosampler is the automatic version for when the user has many samples to analyze or when manual injection is not practical

## Slide 7
High pressure pump .
Injector .
Chromatographic column .
Detector .
Personal computer to read data of component

## Slide 8
Column:
Considered the “heart of the chromatograph” the column’s stationary phase separates the sample components of interest using various physical and chemical parameters.
The small particles inside the column are what cause the high backpressure at normal flow rates.
The pump must push hard to move the mobile phase through the column and this resistance causes a high pressure within the chromatograph

## Slide 9
Detector:
The detector can see (detect) the individual molecules that come out (elute) from the column.
A detector serves to measure the amount of those molecules so that the chemist can quantitatively analyze the sample components.
The detector provides an output to a recorder or computer that results in the liquid chromatogram (i.e., the graph of the detector response).

## Slide 10
Computer:
Frequently called the data system, the computer not only controls all the modules of the HPLC instrument but it takes the signal from the detector and uses it to determine the time of elution (retention time) of the sample components (qualitative analysis) and the amount of sample (quantitative analysis)
chromatogram

## Slide 11
What is HPLC used for?
Separation and analysis of non-volatile or thermally-unstable compounds
HPLC is optimum for the separation of chemical and biological compounds that are non-volatile
Typical non-volatile compounds are:
Pharmaceuticals like aspirin, ibuprofen, or acetaminophen (Tylenol)
Salts like sodium chloride and potassium phosphate
Proteins like egg white or blood protein
Organic chemicals like polymers (e.g. polystyrene, polyethylene)
Heavy hydrocarbons like asphalt or motor oil
Many natural products such as ginseng, herbal medicines, plant extracts
Thermally unstable compounds such as trinitrotoluene (TNT), enzymes
NOTE:
If a compound is volatile (i.e. a gas, fragrance, hydrocarbon in gasoline, etc.), gas chromatography is a better separation technique.

## Slide 12
What is HPLC used for?
Quantitative Analysis
The chart displaying the time-dependent change in signal intensity as a result of the separation is called a "chromatogram".
The measurement of the amount of a compound in a sample (concentration);meaning, how much is there?
The most common parameter for compound ID is its retention time(the time it takes for that specific compound to elute from the column after injection)
Depending on the detector used, compound ID is also based on the chemical structure, molecular weight or some other molecular parameter.

## Slide 13
There are two main ways to interpret a chromatogram (i.e. perform quantification):
Determination of the peak height of a chromatographic peak as measured from the baseline
Determination of the peak area (see figure below);In order to make a quantitative assessment of the compound, a sample with a known amount of the compound of interest is injected and its peak height or peak area is measured

## Slide 14
In many cases, there is a linear relationship between the height or area and the amount of sample.