## Slide 1
جامعة بغداد
كلية التربية للعلوم الصرفة/ابن الهيثم
قسم علوم الحاسبات
المرحلة الاولى
تركيـــــب الحاســـــــــــــوب
2025-2024
المحاضرة الثالثة
TYPES OF MEMORY
أ.م. سميره شمس

## Slide 2: TYPES OF MEMORY
1- Random Access Memory (RAM): The main memory in a computer. It keeps system software, programs and data, which are need when the computer is working. It is a volatile memory.
RAM is divided into same sized locations that each of them has a unique address.
There are two type of RAM:
Dynamic RAM (DRAM):
DRAM chips must be recharged many times each second, or they will lose their contents.
Static RAM (SRAM):
SRAM does not need to be recharged and can hold its contents longer, faster than DRAM, but it is more expensive.

## Slide 3: TYPES OF MEMORY
2-Read Only Memory (ROM): Nonvolatile chips and cannot write on it. It content a set of startup instructions and also contents of system BIOS (Basic Input Output System).
There are three types of nonvolatile:
Programmable read - only memory (PROM): Programmed only once for a specific program if got any change on this program will ignore and replaces, and also called one-time programmable ROM (OTP).
Erasable programmable read-only memory (EPROM): Is a special type of PROM, Programmed several times, can change and delete it by using special devices and ultraviolet rays to change information.

## Slide 4: TYPES OF ROM
Electrically erasable programmable read-only memory (EEPROM): Is based on a similar structure to EPROM, but allows its entire contents to be erased, and then rewritten, so that they not need to be removed from the computer, and also called flash memory.

## Slide 5: Cache Memory
Moving data between RAM and the CPU's registers is very important operation depend on the time which the CPU perform, because RAM, is much slower than the CPU. A partial solution to this problem is to found cash memory, it is similar to RAM in their work, except that it is extremely fast compared to RAM.
Flash Memory:
Flash memory is a type of (EEPROM) is a non-volatile computer storage medium that can be erased and reprogrammed. Flash memory offers fast read access times. It features that it does not need to be defined or programs to run.

## Slide 6: Virtual Memory
If your computer lacks the random access memory (RAM) needed to run a program or operation, Windows uses virtual memory to compensate.
Virtual memory combines your computer’s RAM with temporary space on your hard disk.
When RAM run slow, virtual memory moves data from RAM to a space called a paging file. Moving data to and from the paging file frees up RAM to complete its work.
The more RAM your computer has, the faster your programs will generally run. If a lack of RAM is slowing your computer, you might to increase virtual memory to compensate. However, your computer can read data from RAM much more quickly than from a hard disk, so adding RAM is a better solution.

## Slide 7: BIOS & CMOS
Basic Input Output System (BIOS): Is a set of instructions that a Personal Computer (PC) uses to successfully start up. It is located on a chip on the motherboard inside of a computer.
One of the main functions of the BIOS is to give instructions for the Power-On Self Test (POST). This self test ensures that the computer has all of the necessary parts and functionality needed to successfully start itself, such as use of memory and a keyboard and other components.
If errors are detected during the test, the computer gives a code that reveals the problem. Error codes are typically presented as a series of beeps heard shortly after startup.

## Slide 8: BIOS & CMOS
The BIOS also works to give the computer basic information about how to interact with some critical components, such as hard drives and memory, needed to load the Operating System (OS).
The basic instructions have been loaded and the self-test has been passed, the computer can proceed with loading the OS from one of the attached drives.

## Slide 9: Complementary Metal- Oxide- Semi-Conductor (CMOS)
A complementary metal oxide semiconductor (CMOS) :
is a type of integrated circuit technology. The term is often used to refer to a battery-powered chip found in many personal computers that holds some basic information, including the date and time and system configuration settings, password, needed by the basic input/output system (BIOS) to start the computer.

## Slide 10: Compare between Bios and CMOS
CMOS Chip:
Store the information needed by the BIOS, such as the size of disks and so on and need a battery to retain its contents.
BIOS chip:
Store BIOS system which return at the beginning of the computer the next time and do not need a battery to retain its contents.