## Slide 1: Chemical tests for urine
College of pharmacy /university of Baghdad Biochemistry
third stage - 2nd semester
Lab 5
Presented by
Lecturer Aminah Ali
Blood in urine
(Hematuria, Hemoglobinuria, and Myoglobinuria)

## Slide 2: Learning Objectives & Acquired Skills
Define hematuria and hemoglobinuria
Explain the biochemical dipstick principle
Perform urine microscopy interpretation
Differentiate using lab findings
Apply clinical correlation in diagnosis
Notes: Students should gain diagnostic interpretation skills.

## Slide 3: Introduction & Definitions
• Hematuria: Presence of intact Red Blood Cells (RBCs) in the urine.
o Macroscopic: Visible to the naked eye (red/brown).
o Microscopic: Visible only under a microscope (>3 RBCs/HPF).
• Hemoglobinuria: Presence of free hemoglobin in the urine, usually due to intravascular hemolysis or lysis of RBCs in the urinary tract.
• Myoglobinuria: Presence of muscle hemoglobin (myoglobin) due to muscle injury; often mimics hemoglobinuria.
.

## Slide 4: Detection Methods
The Visual Inspection & Centrifugation
The Chemical Detection (Dipstick and Benzidine Test)
The Microscopic Examination
The Ammonium Sulfate Test
Notes: Blood ketone measurement is preferred in diabetic ketoacidosis as it detects β-hydroxybutyrate.

## Slide 5
The first step in detection is the Centrifugation Test.
• Procedure: Centrifuge a fresh urine sample at 1,500–3,000 RPM for 5 minutes.
• Observations:
1. Hematuria: The red cells settle at the bottom (Red Sediment); the liquid above (Supernatant) becomes clear.
2. Hemoglobinuria: The red cells do not settle; the Supernatant remains red/pink.
Visual Inspection & Centrifugation

## Slide 6: Chemical Detection (Dipstick)
Principle: The Pseudoperoxidase Activity of Hemoglobin
Reaction: The reagent strip contains a chromogen (like tetramethylbenzidine) and an organic peroxide.
Hemoglobin acts as a catalyst (peroxidase-like) to release oxygen from the peroxide, which then oxidizes the chromogen to produce a color change (usually yellow to green/blue).
Reaction Formula:
H2​O2​+ChromogenHb/Myoglobin​Oxidized Chromogen+H2​O
Note: This test detects both hematuria and hemoglobinuria. Hematuria often appears as "speckled" spots on the pad, while hemoglobinuria shows a uniform color change.

## Slide 7: Urine Dipstick (Reagent Strip) Method
Hematuria (RBC)
Hemoglobinuria

## Slide 8
Principle of the Benzidine test
Hemoglobin has peroxidase activity, which releases nascent oxygen from H2O2. Nascent oxygen oxidizes Benzidine in an acid solution to form blue dye
Chemical Detection (Benzidine Test)

## Slide 9: Microscopic Examination
Principle: Physical Identification of Formed Elements
Process: Urine is centrifuged, and the sediment is examined under high power (40x).
• Detection:
Hematuria: Presence of >3 RBCs per high-power field (HPF).
Hemoglobinuria: Absence of intact RBCs despite a positive chemical dipstick test.

## Slide 10: The Ammonium Sulfate Test
Principle: Differential Precipitation
Used to distinguish between Hemoglobinuria and Myoglobinuria (which both turn dipsticks positive).
Procedure: 1. Add 2.8g of Ammonium Sulfate to 5ml of centrifuged urine. 2. Filter or centrifuge again.
Result:
Hemoglobin: Large molecules; they precipitate out. The supernatant turns clear.
Myoglobin: Small molecules; they stay in solution. The supernatant remains red.

## Slide 11: Summary of Diagnostic Flow
1. Red Urine → Centrifuge.
2. Red Sediment? → Hematuria (Confirmed by Microscopy).
3. Red Supernatant? → Hemoglobinuria or Myoglobinuria.
4. Dipstick Positive but no RBCs? → Perform Ammonium Sulfate test or check Plasma color (Hemoglobinuria usually has red/pink plasma).

## Slide 12: Comparison: Hematuria vs Hemoglobinuria vs Myoglobinuria
Feature | Hematuria | Hemoglobinuria | Myoglobinuria
RBCs in Microscopy | Present | Absent | Absent
Dipstick Test | Positive | Positive | Positive
Common Cause | UTI, Stones | Hemolysis | Muscle injury
Notes: Emphasize importance of microscopy in differentiating conditions.
All three give positive dipstick due to heme reaction.
Clinical history is essential for correct diagnosis.

## Slide 13
A urine sample is prepared by adding a few drops of real blood to D.W
Blood in urine (hematuria and hemoglobinuria) test

## Slide 14
Benzidine Test (-ve result)
2ml urine + few drops glacial acetic acid  saturate with benzidine powder  0.5ml H2O2  No change color(-ve result)
Blood in urine (hematuria and hemoglobinuria) test procedure
Benzidine Test (+ve result)
2ml urine + few drops glacial acetic acid  saturate with benzidine powder  0.5ml H2O2  blue to green color (+ve result)

## Slide 15: Clinical Significance
• Hematuria Causes: Renal stones, trauma, glomerulonephritis, malignancy (bladder/kidney cancer), or UTIs.
• Hemoglobinuria Causes: Hemolytic anemia, transfusion reactions, severe burns, or malaria ("Blackwater fever").
Myoglobinuria Causes: Rhabdomyolysis, Crush injuries, Severe exercise-induced muscle damage.

## Slide 16: References
Tietz Textbook of Clinical Chemistry and Molecular Diagnostics
Harper's Illustrated Biochemistry
Henry's Clinical Diagnosis and Management by Laboratory Methods
WHO Laboratory Guidelines

## Slide 17: Thanks for listening